## Slide 1
Virtual Automotive OTA Demo
Production-style OTA orchestration with zonal vehicle model, DoIP, VCAN/CAN FD, UDS, ISO-TP, A/B flashing, Uptane-style trust, MQTT/HTTPS cloud control, and optional Mender trigger
What this demo shows
TCU acts as the in-vehicle OTA orchestrator.
ECUs are updated through realistic transport layers: DoIP or VCAN/CAN FD + ISO-TP + UDS.
Zones, dependency planning, ECU availability, partial rollout, A/B activation, and trust validation are all visible.
The demo is production-style and runnable, but not a full AUTOSAR or hardware-flash implementation.

## Slide 2
Demo Purpose
Why we built it
Show how an automotive OTA platform coordinates cloud, TCU, gateway, zones, and ECUs.
Make protocol layers visible instead of hiding them behind vendor tools.
Demonstrate skip, abort, partial rollout, and dependency-aware decisions from live vehicle state.
What it is not
Not full AUTOSAR DCM/FBL.
Not real hardware flash driver integration.
Not OEM production PKI or TSN/VLAN Ethernet.
It is a realistic integration simulator for architecture, behavior, and demo execution.

## Slide 3
Architecture Diagram
OTA Cloud Server
HTTPS artifacts + MQTT notify/status
TCU Orchestrator
campaign validation, trust, dependency plan, transport selection
DoIP Backbone
UDP discovery + TCP diagnostics
VCAN / CAN FD / ISO-TP
diagnostic path for CAN-based update
Zone Controllers
health, policy, heartbeat, request forwarding
Gateway ECU
A/B slot + flash model
BCM ECU
UDS server + flash target
Cluster ECU
UDS server + flash target

## Slide 4
Architecture Flow In Detail
1. Cloud publishes campaign/job and hosts artifacts over HTTPS.
2. TCU receives trigger by MQTT or Mender deployment, then downloads campaign and firmware.
3. TCU verifies repository state, metadata trust, inventory, compatibility, and dependency order.
4. TCU selects transport: DoIP backbone or VCAN/CAN FD path.
5. Zone controllers enforce ECU heartbeat availability and service/programming policy.
6. ECU programming follows UDS-oriented flow: session -> security -> erase -> download -> transfer -> verify -> activate -> reset.
7. ECU installs into inactive A/B slot; post-install validation commits or rolls back.
8. Final result is reported back through status APIs / MQTT / Mender view.

## Slide 5
Scenario 1: All ECUs Healthy And Eligible
Setup
Topology: default
Dependency: topology default
Offline ECUs: none
ECU state: fresh baseline
Transport: DoIP or VCAN
Expected behavior
Discovery finds all 3 ECUs.
Compatibility passes.
Topological order is built.
Gateway, BCM, and Cluster are flashed and verified.
All move to target version and committed slot.
Presenter message
This is the reference happy-path OTA execution.
It proves orchestration, transport, flashing, and commit flow end-to-end.

## Slide 6
Scenario 2: Some ECUs Already At Target Version
Setup
Use ECU-state presets such as:
Gateway + BCM already updated
Gateway + Cluster already updated
BCM + Cluster already updated
Expected behavior
TCU discovers live ECU versions.
ECUs already at target are classified as ALREADY_SATISFIED and skipped.
Only remaining compatible ECUs are updated.
This is dynamic skip/update, not a hardcoded replay.
Presenter message
This demonstrates production-style delta targeting: do not reflash ECUs that already satisfy campaign target.

## Slide 7
Scenario 3: Some ECUs Are Not Running / Offline
How we trigger it
Dynamic launcher offline menu
or live fault injection:
ecu_fault_control.py <ecu> heartbeat off
Zone controller then marks ECU OFFLINE after heartbeat timeout.
Expected behavior
Cluster offline: may be skipped if campaign policy allows it.
BCM offline: may abort if BCM is mandatory or dependency-critical.
Gateway offline: typically abort because the main dependency path is unavailable.
Presenter message
The fault injection is manual, but the detection and OTA reaction are automatic.

## Slide 8
Scenario 4: Condition Mismatched / Campaign Rejected
Typical mismatch cases
Transport unsupported for selected target.
Bootloader minimum not satisfied.
Mandatory ECU not found or not reachable.
Runtime ECU state preset does not match actual live version state.
Expected behavior
TCU fails validation early.
Campaign is rejected or narrowed before flashing.
Unsafe or inconsistent rollout does not proceed.
Presenter message
This slide proves the system does not blindly push firmware when safety or consistency checks fail.

## Slide 9
Trigger Paths For The Demo
Local dynamic trigger
run_dynamic_demo.sh
Choose topology, dependency, offline case, ECU state, and transport.
Backend job is then published over MQTT and artifacts are downloaded over HTTPS.
This is the cleanest live operator path for local presentation.
Mender trigger
run_dynamic_mender_demo.sh
Build scenario-specific .mender artifact from selected runtime scenario.
Hosted Mender deploys to TCU host.
Mender client invokes tcu-ota-module -> TCU OTA orchestration starts.